## Slide 1: Introduction to IoT
Pavel Genevski, Researcher / Architect @ SAP Labs Bulgaria February, 2018

## Slide 2: Teachers
SAP Labs
  Pavel Genevski
  Vladimir Savchenko
  Hristo Kirilov
  Vladimir Nachev
FMI
  Trayan Iliev

## Slide 3: Administrative Q&A
Кога?
  Четвъртък от 17:00 до 21:00
Къде?
  Зала 320
Как да минем?
  Защита на групов проект + quizzes / индивидуални впечатления

## Slide 4
Let’s get started!

## Slide 5: Over 20 billion connected devices
Consumer market: ~$546B
  1.4B smartphones (flat*)
  157M tablets (7% decline)
  21M smartwatches (flat*)
  Industrial market: ~$868B
  Factories (Industry 4.0)
  Logistics
  Meters
  Trains
  Cities
  ….
Source: https://www.ncta.com/sites/prod/files/GROWTH_IOT-091516-IF-2000w.png
Notes:   https://www.ncta.com/sites/prod/files/GROWTH_IOT-091516-IF-2000w.png
  http://www.scmp.com/tech/article/2067481/smartwatch-market-hits-record-211-million-sales-2016-apple-pulls-ahead-Samsung (Garmin 360% up)
  http://www.pcworld.com/article/3167268/internet-of-things/as-iot-sales-surge-consumers-still-lead-the-way.html
  http://www.sap.com/bulgaria/solution/internet-of-things.html
  http://www.forbes.com/sites/louiscolumbus/2016/11/27/roundup-of-internet-of-things-forecasts-and-market-estimates-2016/#52248474ba55

## Slide 6: How did we get here?
Hardware is now …
  Cheaper
  Smaller
  More connected
  Less power hungry
  Easier to develop
  Ecosystem
  More knowledge
  More opportunities
  More investment
Source: http://www.hamiltonproject.org/ee-ce-image/made/assets/img/uploads/charts/cost_of_computing_power_equal_to_an_ipad2_1017_685_80.jpg
Notes:   http://www.hamiltonproject.org/ee-ce-image/made/assets/img/uploads/charts/cost_of_computing_power_equal_to_an_ipad2_1017_685_80.jpg

## Slide 7: What is IoT?
Physical
  Sensors, Actuators
Connected
  WiFi, Bluetooth, Cellular, LPWAN …
Programmable
  Arduino, C/C++, Python, Java, Assembly ..
  (Atmel, Espressif, TI, Microchip, MIPS, ARM …)

## Slide 8: Industrial vs Consumer IoT
Industrial IoT
  Drivers: cost and risk reduction, business agility, informed decision making
  Challenges: security, compliance, compatibility, reliability, connectivity, support …
Consumer IoT
  Drivers: coolness, convenience, health, some cost reduction
  Challenges: UX, hype vs value, time to market, some privacy and security
Source:http://www.clipartpanda.com/clipart_images/stacks-of-money-clipart-1-57831954
Notes: http://www.clipartpanda.com/clipart_images/stacks-of-money-clipart-1-57831954
http://www.clipartpanda.com/clipart_images/anime-manga-rock-star-guitar-38034053

## Slide 9: Industrial IoT examples
Predictive maintenance & Remote management
  Solar & wind power, pipelines, bridges, facilities, vehicles, crops …
Smart utilities (meters)
  Remote and continuous metering of water, electricity, gas …
Source: http://www.metering.com/wp-content/uploads/2016/05/smart-meters-768x510.jpg
Notes: http://www.triplepundit.com/2016/04/beyond-energy-savings-smart-buildings-triple-threat-2/
http://www3.weforum.org/docs/WEFUSA_IndustrialInternet_Report2015.pdf
Drones are used for many monitoring tasks
There is an insurance use case for vehicle monitoring (both rent-a-car and cu
http://cdn.phys.org/newman/gfx/news/hires/2012/optimalplann.jpgstomer…). It is about differential pricing and disaster avoidance (e.g. in Australia)
http://www.metering.com/wp-content/uploads/2016/05/smart-meters-768x510.jpg

## Slide 10: Industrial IoT examples contd.
Smart buildings
  HVAC, lighting, security & access control, safety monitoring, indoor positioning …
Smart City
  Pollution, traffic, controlling, services …
Source:http://blueapp.io/wp-content/uploads/2016/08/How-IoT-optimize-building-performance-with-in-minimal-operational-cost.jpg
Source: http://www.libelium.com/libelium-images/generico2/sensor_polvo-490.png
Notes: http://www.libelium.com/libelium-images/generico2/sensor_polvo-490.png
http://blueapp.io/wp-content/uploads/2016/08/How-IoT-optimize-building-performance-with-in-minimal-operational-cost.jpg

## Slide 11: Consumer IoT examples
Personal productivity & fashion
  Smartphones, smartwatches …
Home Automation
  Smart locks, Bulbs, Smart TVs, Baby monitors…
Source: https://42xaiz2iny9m45jqzf36ofk2-wpengine.netdna-ssl.com/wp-content/uploads/2014/08/Front.jpg
https://c.slashgear.com/wp-content/uploads/2011/12/NO-4.jpg
Notes: https://42xaiz2iny9m45jqzf36ofk2-wpengine.netdna-ssl.com/wp-content/uploads/2014/08/Front.jpg
https://community.rapid7.com/community/infosec/blog/2015/09/02/iotsec-disclosure-10-new-vulns-for-several-video-baby-monitors
https://c.slashgear.com/wp-content/uploads/2011/12/NO-4.jpg

## Slide 12: Consumer IoT examples contd.
Sports & Health
  Fitness & health trackers
  Professional sport gadgets
Connected cars …
  Predictive maintenance, accident reaction, theft protection …
Source: https://tctechcrunch2011.files.wordpress.com/2014/11/victoria-secret-heart-rate-bra.jpg?w=738
https://cochlearimplanthelp.files.wordpress.com/2015/04/mi-band.jpg,
http://d3dc23s9xv125m.cloudfront.net/images/baseball/baseball_setup_connect@2x.pngTesla

## Slide 13
What?
Notes: https://gearjunkie.com/legacy/images/21010.jpg
https://tctechcrunch2011.files.wordpress.com/2014/11/victoria-secret-heart-rate-bra.jpg?w=738
https://cochlearimplanthelp.files.wordpress.com/2015/04/mi-band.jpg

## Slide 14: Course assignment
Objectives
  Challenge yourself. No idea is too brave!
  Try to make something useful
  Learn new things
Examples
  Smart beehive, A/C monitoring
  Smart home / company / city
  You name it …
?
Source: https://www.smartbin.com/markets/level-sensor-general-waste-recyclables/, LG air conditioners
Notes: https://www.smartbin.com/markets/level-sensor-general-waste-recyclables/

## Slide 15
How?
Notes: https://gearjunkie.com/legacy/images/21010.jpg
https://tctechcrunch2011.files.wordpress.com/2014/11/victoria-secret-heart-rate-bra.jpg?w=738
https://cochlearimplanthelp.files.wordpress.com/2015/04/mi-band.jpg

## Slide 16: IoT development platforms
Android & iOS
  Phones, wearables, TVs …
Linux
  Raspberry PI, Beaglebone …
RTOS
  FreeRTOS, Nucleus …
Bare metal
  Vendor SDKs: Espressif, NXP, TI, Atmel, Microchip …
  Arduino: Atmel, ESP8266 (we will use this one)
Notes: http://energia.nu/

## Slide 17: Sensors
So many sensors …
  Touch, movement, compass, acceleration, video, sound
  Temperature, humidity/moisture, light / infrared
  Pressure, gas detection,
  Force (tenso), proximity, motion
  Liquid level, flow, magnetic field (hall), radiation
  Fingerpring, heart rate …
Source: http://www.imagesco.com/geiger/buying-a-geiger-counter-pg3.html, http://www.greyline.com/twotechnologies.htm, http://www.noshok.com/force_2351_series.shtml
Notes: http://www.imagesco.com/geiger/buying-a-geiger-counter-pg3.html
http://www.greyline.com/twotechnologies.htm
http://www.noshok.com/force_2351_series.shtml

## Slide 18: Sensors characteristics
Functional
  Range
  Accuracy
  Precision (repeatability, noise)
  Resolution & Sensitivity
  Speed
  Non-functional
  Longevity & Reliability (MTBF, triplication)
  Power consumption
  Price
  Op. environment: combustive, corrosive, military
Source: https://www.slideshare.net/akashmaurya24/shashank-soni-sensors-presentation
Notes: http://kb.mccdaq.com/KnowledgebaseArticle50043.aspx
https://www.slideshare.net/akashmaurya24/shashank-soni-sensors-presentation
http://www.ni.com/white-paper/14860/en/

## Slide 19: Connectivity (media access)
Long range
  LoRaWAN, Sigfox, 6LoWPAN (868MHz), 3G/GPRS
Medium range
  ZigBee, WiFi
Short range
  Bluetooth 4.0/BLE, NFC/RFiD
Wired
  Ethernet, RS-485, 4-20 mA …
Source: http://hitlistsofts.blogspot.bg/2015/05/difference-between-gsm-gprs-edge-3g.html
Notes: http://www.libelium.com/products/waspmote/
http://hitlistsofts.blogspot.bg/2015/05/difference-between-gsm-gprs-edge-3g.html

## Slide 20: Connectivity (application)
HTTP (REST)
CoAP
  Stripped down, datagram based HTTP over UDP/SMS …
  Goal: Interop with the web
MQTT
  Open standard, Client/server (broker), pub/sub
  SSL/TLS, user/pass auth
Many others: IRC, XMPP, AMQP …
CoAP

## Slide 21: Data management and analytics
Data ingestion
  Edge processing, batching & compression
  Data ingestion: Kafka, HDFS, Cassandra …
Analytics
  Spark/Hadoop, Python
  Keras, Theano, TensorFlow …
Visualization
  Matplotlib
  D3 + plugins (e.g. c3js)
  Dygraphs, Flot

## Slide 22: Security
http://1.bp.blogspot.com/-1EN9zxdS6PQ/UKJSChMxu9I/AAAAAAAABEk/wheTrU34TBU/s640/I+am+Hacker.jpg
Notes: http://1.bp.blogspot.com/-1EN9zxdS6PQ/UKJSChMxu9I/AAAAAAAABEk/wheTrU34TBU/s640/I+am+Hacker.jpg
http://www.prophethacker.com/wp-content/uploads/2016/04/Hacker-silhouette.jpg

## Slide 23: Who’s the hacker?
Motivation
  Emotion
  Profit
  Scientific interest
Black hats vs White hats
  Damage
  Money flow
  Breaking the law?
Cyber war
Invested resources
Expected profit
Wannabes
Spammers
Security researchers
Industrial espionage
Governments espionage
Competitors

## Slide 24: Solution?
No silver bullet
Balance between risks and profits
Learn from the others’ mistakes
Plan countermeasures
Source: https://www.youtube.com/watch?v=WyM2r-ixDvg

## Slide 25: Showcase: Self aiming, social rifle …
Hackers: Runa Sandvik & Michael Auger
Target: 2013 TrackingPoint TP750 WiFi rifle
Payload:
  Detune scope (e.g shoot wrong target)
  DoS the entire scope
Source: http://adrenaline.uol.com.br/files/upload/noticias/2015/07/mateus/sniper-pc_2.jpg
Notes: https://www.blackhat.com/docs/us-15/materials/us-15-Sandvik-When-IoT-Attacks-Hacking-A-Linux-Powered-Rifle.pdf
https://www.youtube.com/watch?v=ZcukSF7ruZY

## Slide 26: Hacks
WiFi hotspot
  WPA2 key is guessable and can’t be changed
Mobile API (tune ammo weight etc. )
  “Secret” admin commands, one of which opens the SSH port
Raw backend access
  Tune ammo weight without validation (persistently and without validation)
Firmware updates
  GPG signed, but private key is on the device
Notes:   SSID contains serial number

## Slide 27: Vendor’s official response
  You can continue to use WiFi if you are confident no hackers are within 100 feet.

## Slide 28: Stuxnet … an APT
Hackers: No Such Agency
Target: Iran’s Natanz uranium enrichment centrifuges
Attack: Spin rate could be controlled. Monitoring data tampered.

## Slide 29: Hack details - infection
Windows shortcuts can reference an icon in a DLL
Windows uses LoadLibrary to load the icon from DLL
Result: malicious DLL executed with local user’s privileges
DLL file with icons
Notes:   11:30
  Note: you don’t have to click the shortcut, but merely put the flash drive and it would even load DLLs from the internet using WebDAV).
  Fix2 was to move from CRC32 to SHA256
  https://www.youtube.com/watch?v=SD1J8LrkQJE
  http://superuser.com/questions/335685/bizarre-shortcut-icon-problem-with-xp-7-dual-boot
  https://chrlvclaudiu.wordpress.com/2010/08/19/exploit-microsoft-windows-automatic-lnk-shortcut-file-code-execution/
  http://cve.mitre.org/cgi-bin/cvename.cgi?name=CVE-2010-2568
  https://technet.microsoft.com/en-us/library/security/ms15-020.aspx
  http://stackoverflow.com/questions/1515914/crc32-collision

## Slide 30: Hack details – privilege escalation
Windows Vista+
  Scheduled tasks are stored in XML files that are read/writeable by user
  Task’s target user account is specified in the file
  Files are CRC32 checksum validated before execution (sum stored in registry)
Windows XP
  Keyboard layouts can be installed from any location (not just %SYSTEM%)
  They contain an unvalidated function pointer index that the kernel trusts
  Manipulating the index makes the kernel run code located in user space

## Slide 31: Hack details – spread
All Windows versions
  Copy to remote shares, USB drives etc.
Windows XP
  A remote “Print to file” using a Guest account is possible
  New MOF files in System32\wbem\MOF are compiled and executed under system privileges.
Notes:   http://poppopret.blogspot.com/2011/09/playing-with-mof-files-on-windows-for.html

## Slide 32: Hack details – payload
Target
  Siemens Simatic 6ES7-315-2 PLCs
  Natanz specific configuration (cascade size >155, frequency > 1000Hz)
  Result: no collateral damage in other plants
Payload
  Increase spin rate from 1000 to 1410Hz for 15 min. Then sleep 27 days.
  Decrease the spin rate to 5Hz for 50 min. Sleep another 27 days.
  Report normal readings to the plant monitoring system
  Result: ~1000 (out of ~16000) rotors cracked in a just a few months
Notes:   17:40
  http://www.thetower.org/2545-iran-stops-dismantling-centrifuges-at-two-uranium-enrichment-plants/
  (out of ~19000)
  https://www.youtube.com/watch?v=wapd1-E5dzc

## Slide 33: IoT specific security concerns
Doom’s day scenarios
  e.g. Natanz
Privacy attacks
  Samsung TV, Amazon Echo
IoT botnets
  Devices turn to DDoS zombies (Mirai botnet -> 100K nodes)
Business risk & disruption
  Bricked devices
  Limited ability to update crypto (due to e.g. vendor, power, computing)
  Wider the security perimeter

## Slide 34: Possible security counter measures
Before the fact: Make attacker’s life harder
  Strong crypto, SSO, 2FA
  OWASP Internet of Things
  Pentest hardware too (Logic analyzers, SDR …)
After the fact: Plan for mitigation
  Technical (DDoS protection, device blacklisting, recall and factory reset)
  PR & Legal (Ready made responses, limitation of liability)
  Financial (Insurance, indemnification from partners)
Notes: http://www.grandideastudio.com/wp-content/uploads/secure_embed_paper.pdf

## Slide 35: Device management
Problems being solved
  Secure device onboarding & off-boarding / blacklisting
  Maintenance:
    OTA updates, restarts
    Diagnostics: uptime/heartbeat, network quality (latency, error rate)
    Locating a device
    Bulk operations scheduling & maintenance plans …
Solutions
  OpenHAB, Kura
  Blynk, Thingspeak, Beebotte, SAP, IBM …
  And probably lots of home grown stuff due to specifics of business

## Slide 36: Thank you
Contact information:
Pavel Genevski
Researcher / Architect
SAP Labs Bulgaria

## Slide 39: The Grid
Drawing area
Headline area
White space